## Slide 1: Coupling free flow and pore flow: Averaging of pore-scale results to obtain effective interface parameters and to validate macroscale models SFB 1313 Summer School 2021 27th September

## Slide 2: Coupled free-flow and pore-flow systems
Surface/subsurface interactions
Blood flow through body tissues
Water/gas management in fuel cells
Industrial water filtration
https://ww.thermalcare.com; https://ufz.de; https://techetch.com/fuel-cells/; 23.09.2021

## Slide 3: How can one model a coupled free-flow pore-flow system?
Two Domain
Hybrid Coupled
Single Domain
Coupled (Multi-Domain)
Pore scale:
Macroscale (REV):
…Expensive!
…Very quick, not expensive!
or

## Slide 4: What are the (macroscale) coupling conditions?
Two Domain Approach (REV)
Stokes
Classical conditions (Beavers & Joseph (1967))
Effective parameter needs to be determined
Alternative conditions a) Angot et al. (2017), Ochoa-Tapia & Whitaker (1995), …  Effective parameters need to be calibrated b) Jäger & Mikelic (1996), Lacis & Bagheri (2017), Eggenweiler & Rybak (2021), Sudhakar et al. (2021), …  Effective parameters are computed
Pore-scale simulations for determination of effective parameters (a) & validation of macroscale models (a,b)
„The appropriate averaging of the pore-scale flow field is still an open question.“
- Ugis Lacis (J. Fluid Mech., 2021, preprint)

## Slide 5
Averaging techniques for pore-scale solutions
Volume averaging (classical and adaptive VA)
Pore-scale solutions integrated over REV
Averaged value obtained as
From Preprint: Rinehart et al. :“The Brinkman viscosity for porous media exposed to a free flow”, 2021.
Line averaging (Plane/Horizontal Averaging)
Average pore-scale solution over lines in the horizontal direction
Mainly used for 1D flows
Combination line/volume averaging

## Slide 6
Ensemble averaging
Averaging samples are generated by moving the solid inclusions in horizontal direction
With N as the number of averaging samples, the averaged value is obtained as
But, which averaging method is “correct“ for:
(a) Obtaining Effective parameters?
(b) Obtaining validation data?
Averaging techniques for pore-scale solutions

## Slide 7: a) Effective parameter α
b) Validation
Investigate different averaging techniques to find & compare results
Use alternative coupling conditions: - Conditions of Angot et al. (2017) for can be used for 1D flows: in Angot et al. (2021) calibration of α - Conditions from Eggenweiler & Rybak (2021) can be used to compute for isotropic media ():
Investigate different averaging techniques & compare averaged results
Comparison with alternative coupling conditions where all effective parameters are computed, e.g., Lacis & Bagheri (2017), Eggenweiler & Rybak (2021), Sudhakar et al. (2021)

## Slide 8
Start case: Laminar, pressure-driven, parallel flow, 2D
Where to start?
Pore-scale simulations
Averaged pore-scale results
Coupled REV-scale simulations
REV-scale results, classical IC based on BJ
How can we define based on the averaged pore scale? Based on comparison of pore-scale and macroscale concepts, how can we assess the suitability of for the near interface free flow?

## Slide 9
Pore-scale simulations
Coupled REV-scale simulations
In which other cases would the same methods be relevant?
Which other coupling conditions can be tested?
Averaged pore-scale results
REV-scale results, classical IC based on BJ condition

## Slide 10
Plans for the next two weeks
We will have a guest visiting for a week from KTH, Ugis Lacis.
Guest speaker presentation:
Thursday morning, 9:30-11:30
Implement and test different techniques
Evaluate results using macroscale models
Consider different configurations
Flow directions
Flow regimes
Geometries
Find optimal averaging techniques for averaging pore-scale results